# Manual for euroduino “sigan” program

## Description

It is primarily used for trigger / gate generation with variable and CVable gate length / pulse width. Two channels (DIG OUT1 and DIG OUT2) generates clocks. The first is the master clock. The second is “slaved” to the master frequency and outputs gates ONLY when triggered by a signal in DIG IN2 (for example at t0 and t1 on the figure below). Master clock can be driven externally if DIG IN1 receives a clock signal (trigger/gate). As we have never enough random, the two CV OUT give you two random channels driven by the master clock. Different parameters are set via POT1 and POT2 (!!! rules of one knob per function is largely broken !!!) and controlled by voltage via CV IN1 and CV IN2.

DIG OUT1
DIG OUT2
CV OUT1
CV OUT2

DIG IN2
DIG IN2
master clock
slave clock
 - x2 clock multiplier
 - triggered at t0 and t1
Random steppped CV 1
 - x3 multiplier
Random steppped CV 2
 - x1 multiplier
t1
t0

master clock period (freq)
master clock pulse width (PW)
slave period
slave PW
random 1 period
random 2 period

amplitude max

amplitude max

## How to use

Each parameters are accessible via a combination of switches SW1 and SW2. SW1 selects the function and SW2 selects parameters:
- SW1 in high position, clock control
  - SW2 in high position:
    - POT1 control clock frequency of master between 40 and 300 BPM if no clock are detected in DIG IN1. If clock are fed in DIG IN1, POT1 act as external clock divider / multiplier.
    - POT2 control clock frequency of slave as a multiplier of master clock, from x1 to x8
  - SW2 in mid position: POT1 and POT2 attenuate signal from CV IN1 and CV IN2. Incoming CV in CV IN1 and CV IN2 are modulating gate length of master and gate length of slave.
  - SW2 in low position: POT1 and POT2 control respectively gate length of master and slave from 0 to 99% of the clock period.
- SW1 in mid position, digital input and output control
  - SW2 in high position: POT1 and POT2 selects respectively whether channel1 and channel2 clocks are generated on HIGH state (positive voltage) or on LOW state:
    - POT on the left: LOW state
    - POT on the right: HIGH state
  - SW2 in mid position: POT1 and POT2 attenuate signal from CV IN1 and CV IN2. CV IN1 controls slave multiplier and CV IN2 modulates gate length of slave.
  - SW2 in low position: POT1 and POT2 selects respectively whether DIG IN1 and DIG IN2 signaled a clock on rising or falling edge.
    - POT on the left: rising edge
    - POT on the right: falling edge
- SW1 in low position, random control
  - SW2 in high position: POT1 controls frequency (divide/multiply master clock) and POT2 controls random amplitude or maximum random voltage for random1 (CV OUT1).
  - SW2 in mid position: POT1 and POT2 attenuate signal from CV IN1 and CV IN2 that modulates respectively random frequency of random1 and random2.
  - SW2 in low position: same as SW2 in high position but for random2 (CV OUT2)

DIG IN1

CV IN1

DIG IN2

CV IN2

DIG OUT2
Slave output

CV OUT2
Random2 output

DIG OUT1
Master output

CV OUT1
Random1 output
Switch 1
Function selector

Switch 2
Parameter selector

Pot 2

Pot 1

## About the clock divider / multiplier

When the master is driven externally (via DIG IN1) and for the clocks of random channel 1 and 2, the clock rate is calculated with the coefficient selected by the potentiometer as follow:
/8, /7, /6, /5, /4, /3, /2, x1, x2, x3, x4, x5, x6, x7, x8
The slave depends always on master and its clock rate is calculated with the coefficient selected by the potentiometer as follow:
x1, x2, x3, x4, x5, x6, x7, x8
## About the CV

When a CV is connected to the CV input and SW2 is in mid position, the CV applied to the parameter is calculated as follow
parameter = initial_parameter + attenuated(CV)
where
- attenuated(CV) is the CV (from CV IN1 or CV IN2) attenuated by POT1 or POT2
- initial_parameter acts as an offset
## About the broken “one knob per function” rule

Tweaking 12 different parameters might be insanely hard because euroduino module has no visual feedback and only two 2 knobs... Not easy but feasible, just remember that SW2 in mid position does not change any parameter (just attenuates the CV in CV IN1 and CV IN2). Selecting the wrong function with SW1 might happen. To avoid overwriting wrong parameters, keep the SW2 in mid position!

## Patch idea

“burst generator”, generates a series of gate signal in DIG OUT2 when DIG IN2 receives a clock
1. set the frequency of master clock (knob1) and slave clock multiplier (knob2) with SW1 and SW2 in high position
2. send a trig/gate into DIG IN2 and get the succession of trigger/gate from DIG OUT2

“irregular/shuffled clock”
1. set the frequency of master clock (knob1) and set the slave clock multiplier to 1 (SW1 and SW2 in high position)
2. set the pulse width of master clock to around 60% with knob1 (SW1 up and SW2 down)
3. set slave DIG IN2 to be triggered on falling edge with knob2 (SW1 mid and SW2 down)
4. patch the output from DIG OUT1 to input DIG IN2
5. patch DIG IN1 and DIG IN2 in mixer / unity mixer / binary OR module to get the shuffled clock
6. set to taste by tweaking PW parameter as explained in step 2.

“clock multiplier”
1. set the frequency of master clock (knob1) and slave clock multiplier (knob2) with SW1 and SW2 in high position
2. patch the output from DIG OUT1 to input DIG IN2

“triggering MS-20 (or any S-Trig synth) with variable pulse width”
1. patch trigger signal in DIG IN1
2. set DIG OUT2 trigger signal to LOW with knob2 (SW1 mid and SW2 up)
3. set slave pulse width to its minimal requested value with knob 2 (SW1 up and SW2 down)
4. patch DIG OUT2 to MS20 trigger in
5. put module in pulse width CV mode with SW1 up/mid and SW2 mid
6. patch CV in CV IN2 and attenuate with knob2
Note: random channel 1 or 2 can be used as CV, just patch CV OUT1 or CV OUT2 in CV	IN2!

## About compilation

- compile with arduino version 1.6.12 (might not compile with 1.5 and lower)
- need elapsedMillis.h library to be installed. With Arduino GUI, go to Sketch – Include Library – Manage Libraries…, then search for elapsedMillis and install the library